## Slide 1: Integration at the Edge TDM/IP and IP/IP
Moisés Silva
Manager, Software Engineering
msilva@sangoma.com
Technology Summit
Niagara Falls, July 18, 2013

## Slide 2: Agenda
About Sangoma
VoIP deployment challenges
Portfolio of Gateways
Portfolio of Session Border Controllers
Closing

## Slide 3: About Sangoma
Industry pioneer with over 25 years of experience in communications hardware and software
Publicly traded company since 2000
  TSXV: STC
One of the most financially healthy companies in our industry
  Growing, Profitable, Cash on the Balance Sheet, No Debt
Mid-market sized firm with just under 100 staff in all global territories
  Offices in Canada (Toronto), US (NJ), EU (UK & Holland), APAC (India), CALA (Miami)
World Wide Customer base
  Selling direct to Carriers and OEMs
  Selling to the Enterprise through a network of distribution partners

## Slide 4: Broad Line of Great Products
Voice Telephony Boards
  Analog/digital/hybrid, WAN, ADSL, etc
Software Applications
  NetBorder Express, Call Progress Analyzer…
Gateways
  NetBorder SIP to TDM
  SS7 to SIP
Wireless Products
Session Border Controllers
Microsoft Lync
Fiber connectivity (STM1)
Transcoding (boards/appliances)

## Slide 5: Vibrant Ecosystem of Clients & Partners
Contact Center OEM Integration with major software suites
Carriers, Cloud, Data Ntwks Proven Infrastructure Technology
Open Source Telephony Ready to use drivers for Sangoma boards
Proprietary PBX and IVR Plug-in to major soft-PBX and IVRs

## Slide 6: Innovation and Interoperability
Indian Army

## Slide 7: VoIP is now mainstream
Yes, for sure but …
There are still a lot of legacy pockets/islands
We are still in a transition phase from legacy to VoIP
This drives the need to interconnect legacy networks with VoIP Networks
  In the core and at customer premises
And VoIP to VoIP Networks also brings its own set of challenges at the edge

## Slide 8: Typical VoIP Service Provider Network
PSTN
PSTN
IP Peering
SS7
SS7
Voice
Voice
IP Network
Legacy
PBX
VoIP GW
IP PBX
Broadband
Router
Softswitch
VoIP
VoIP
VoIP
VoIP
VoIP
VoIP
VoIP GW
VoIP GW
Peering
Session Border Controller
Core
Access
Access
Session Border Controller
In VoIP Networks, SIP has become the standard of choice

## Slide 9: Integration at the Edge
PSTN interconnection requires VoIP Gateways
  SS7 to VoIP Gateway in the core
  Enterprise VoIP Gateways for customer premises (enterprise, Soho, residential)
    SIP Trunking into legacy PBXs
    SIP to analog line conversion (phones or key systems)
VoIP to VoIP brings its own challenges
  Creates the need for Session Border Controllers
  We will come back on this one later

## Slide 10: Enterprise Gateways
Vega Series

## Slide 11: Vega Series: Telecom Appliances
Vega 50
  H.323 / SIP
  Up to 8 port BRI
  Up 10 ports FXO/FXS combos
Vega 5000
  H.323 / SIP
  24 or 50 ports FXS
  2 FXO failover to PSTN
Vega 100, 200, 400
  8 to 120 VoIP calls H.323 / SIP
  Up to 4 T1/E1 (PRI, CAS)
  Power fail hardware
  Expandability and upgrades
    DSP modules
    Software license

## Slide 12: Features – All Gateways
VoIP Protocols
  SIP or H.323
  TLS / SRTP for security
Dual LAN + Console Port
Management
  Web GUI
  CLI
  RADIUS
  SNMP
  Syslog
  Billing logs
Powerful call routing capabilities
Remote Firmware Upgrade
Vocoding
  G.711, G.729, G.723, G.726
G.168 Echo Cancellation
T.38 Fax relay
Enhanced Network Proxy for failover

## Slide 13: Vega Provisioned for By-Pass
To/From
Telco
E1/T1 cables
Primary Gateway
Hot Stand-By Gateway
E1/T1 cables
Notes: If the Power to the Main Unit Fails the Relays Close [Click]
The Main Unit is now in BYPASS and the Hot Stand-By Unit is handling all call routing. The Main Unit is invisible to the circuit.

## Slide 14: Operating in By-Pass Mode
To/From
Telco
T1/E1 cables
Primary Gateway
Hot Stand-By Gateway
Internal relay trips to connect to by-pass ports

## Slide 15: SIP Trunking
The TDM-Based PBX can use SIP Trunks to reduce cost and improve flexibility
PBX, TDM
Endpoints
Analog
BRI
PRI
ITSP
SIP /
VoIP
Legacy PBX

## Slide 16: SIP Trunking with Resilience
Vega reroutes all calls to the PSTN if:
SIP/WAN/Internet fails
Power Fails to Gateway
Analog
BRI
PRI
ITSP
SIP /
VoIP
PSTN
PBX, TDM
Endpoints
Legacy PBX

## Slide 17: SIP Dial Tone/Multi-Dwelling Units
IP Network
LAN
24 or 50 analog FXS long reach lines
IP Router
Tenant 1
Tenant 2
Tenant 3
Tenant N
Softswitch
Carrier SS7 GW
IP Router
Session Border Controllers
VoIP Service Provider
SS7 PSTN
SIP Peering
MDU

## Slide 18: SNAP TOOL
Sangoma Network Appliance Provisioning Tool simplifies provisioning and deployment of gateways for use on Interoperability Partners’ networks
  Sangoma builds standard configuration files for an Interoperability Partner
  Through the Snap Tool, user provides installation specific info (IP Address, User_Name, Password, etc.)
  Snap Tool automatically builds a provisioning template that can be instantly uploaded to the gateway
We can work with you to add your SIP trunking service on SNAP

## Slide 19: Step One: Select a Carrier

## Slide 20: Step Two: Select Gateway

## Slide 21: Step Three: Add Specifics

## Slide 22: Step Four: Download Template

## Slide 23: SS7 Gateways
NetBorder Series

## Slide 24: NetBorder SS7 Gateway Features
Up to 32 T1/E1 per server
Can scale up to 288 E1s in relay mode where multiple systems act as one
SS7 ISUP Signaling with several national variants
  ITU, ANSI, Bellcore, France, UK, China, India and Russia
Wide range of narrowband and wideband codecs supported
  for any to any codec transcoding
Robust implementation with distribution, failover and redundancy
Flexible XML based routing rules for call control
Coming Features:
  T.38 and SIP REFER support
  Sigtran relay and termination
  Megaco / H.248 support for enhanced Softswitch integration

## Slide 25: Deployment Options

## Slide 26: SS7 Gateway Place on Network
SS7 signaling to gateway is like an SSP on the PSTN network
Signaling connects directly to SSP or STP equipment
  Connects to STP node via an A link (typical North American)
  Connects to SSP node via an F link (typical European)
These are not yet supported: CNAM, LIDB, LNP or anything SCCP (TCAP, MAP or INAP)
Notes: This slide is primarily to educate sales people, and probably should not be presented to customers.
If you are asked about CNAM, LIDB, LNP, or any SCCP functionality, please not the request and forward it to the marketing department for tracking.

## Slide 27: SS7 to VoIP Inter-Working

## Slide 28: Access Gateway for SIP Softswitch
Provides inter-carrier TDM access to SIP-only based Softswitch
Interconnection to several service providers
Centralized call control for carriers in distributed networks
Softswitch performs routing, billing, subscriber management
Notes: Voice may be routed entirely by PSTN, with this solution handling signaling.
RTP may be added to provide cheaper voice transport via IP

## Slide 29: Access Gateway for Megaco Networks
Combined SGW (signalling gateway) and MG (Media Gateway)
Leverages Central Control (MGC) Carrier Infrastructure in large distributed networks
Softswitch (MGC) performs signalling, routing, billing, subscriber management, etc.
Megaco: Media Gateway Control Protocol (aka H.248)
Notes: An alternate method for connecting calls between PSTN networks if Megaco (H.248) is preferred over SIP.

## Slide 30: VoIP to VOIP integration challenges
Integration at the Edge

## Slide 31: End to End VoIP interworking challenges
SIP is it! RFC3261
But while it is the largest RFC around, easy to end up with incompatible SIP end-points
Quick search in RFC for words such as Should, Can, May, Options! It’s pretty loose!

## Slide 32: Other challenges
Solve firewall and NAT issues (ALG) without compromising security / integrity of networks
Normalize sip messaging
Fix errors in the sip messaging stream
Register sip trunks with ITSP
Secure SIP & voice (TLS, SRTP, IPSEC)
Codec conversion
Manage QoS settings and SLA
Provide access to remote users
This is what SBC’s do!

## Slide 33: Security Threats with VoIP
Denial of Services
  Call/registration overload
  Malformed messages (fuzzing)
Configuration errors
  Mis-configured devices
  Operator and application errors
Theft of service / Fraud
  Unauthorized users
  Unauthorized media types
BYOD
  Smartphones running unauthorized apps
  Viruses and Malware attacking your VoIP network
Denial of Services
  Call/registration overload
  Malformed messages (fuzzing)
Configuration errors
  Mis-configured devices
  Operator and application errors
Theft of service / Fraud
  Unauthorized users
  Unauthorized media types
This is what SBC’s do!

## Slide 34: Portfolio of Session Border Controllers

## Slide 35: Session Border Controllers
Vega Enterprise SBC
  25-250 Sessions/Calls
Vega VM Enterprise SBC
  25-500 Sessions/Calls
  Software Only/Virtual Machine Ready
Vega VM/Hybrid Enterprise SBC
  SANGOMA EXCLUSIVE
  25-500 Sessions/Calls
  SBC Maintained in VM
  Media Functions offloaded to external hardware resource
NetBorder Carrier SBC
  250-4000 Sessions/Calls

## Slide 36: SIP Trunking
This NetBorder SBC protects the ITSPs network
Notes: Advantages
  Known demarcation point
  Reduces interop issues/resource with core
  Transcoding if required

## Slide 37: SIP Signalling Conversion
Convert SIP over TCP to SIP over UDP
Some devices require SIP/TCP
  e.g. Microsoft Lync

## Slide 38: SBC For Hosted PBX
Known demarcation point
Reduces interoperability issues with core
Transcoding if required

## Slide 39: SIP Network Peering/ IP Carrier Interconnect
Use IP for inter-carrier links
No TDM conversion required:
  Decrease complexity
  Better voice quality, less delay, less transcoding

## Slide 40: Simple Licensing
Simple per session licensing
  No Per Feature, Per User or Per Codec licensing
Predictable SBC capacity and cost in every use case

## Slide 41: Closing

## Slide 42: Closing
Transition from Legacy to VoIP is still happening
  Drives the need for VoIP Gateway
End-to-end VoIP networks introduce new challenges
  Drive the need for Session Border Controllers
Sangoma provides a portfolio of products that suit small and large service providers

## Slide 43: Thank You!
Questions?